Sampling schemes for instruments in Massachusetts Bay at

# U.S. Geological Survey long-term moorings

| Site | Mooring type | Instrument type | Sampling interval | Variables and sampling scheme |
| --- | --- | --- | --- | --- |
| A | Subsurface | Microcat | 300 s | One sample of T and C every 300 s. |
|  |  | VMCM |  | One sample of V every 300 s. |
|  |  | Seacat | 300 s | One sample of T, C and Tr every 300 s. |
|  |  | Time-series sediment trap | 9 days | Sediment in collection bottle |
|  |  | Tube trap | Deployment | Sediment in trap |
| A | Tripod | ADCP | 900 s | Average of 300 one second pings every 900 s in 2 m bins |
|  |  | MIDAS | 300 s | 300 s averages of V (BASS) and P at .5 Hz. Single sample of T, C and Tr every 300 s. |
|  |  | Camera | 4 hours | Single picture |
|  |  | Tube trap | Deployment | Sediment in trap |
| B | Subsurface | Microcat | 300 s | One sample of T and C every 300 s. |
|  |  | Tube trap | Deployment | Sediment in trap |
|  |  | Time-series sediment trap | 9 days | Sediment in collection bottle |
| B | Tripod | ADCP | 900 s | Average of 300 one-second pings every 900 s in 2 m bins. |

Variables Key:  C = Conductivity; OBS = Optical Backscatter; P = Pressure; T = Temperature; Tr = Light transmission; V = Current velocity.

Instrument Key:  ADCP = Acoustic Doppler current Profiler; MIDAS = USGS Multiparameter Intelligent Data Logging System; SBE-39 = pressure data logger.