Identification_Information:

Citation: CI-87 Vibracores

Citation_Information:

Originator: Jordan M. Sanford

Originator: James G. Flocks

Originator: Jack L. Kindinger

Originator: Mark A. Kulp

Originator: S. Jeffress Williams

Publication_Date: 2008

Title: CI-87 Vibracores

Geospatial_Data_Presentation_Form:

Series_Information:

Series_Name:

Issue_Identification:

Publication_Information:

Publication_Place: St. Petersburg, FL

Publisher: U.S. Geological Survey

Description:

Abstract:

In 1987, the U.S. Geological Survey (USGS), in cooperation with the Louisiana Geological Survey (LGS) and the Louisiana Department of Natural Resources (LDNR), collected 77 12-m-long vibracores to investigate the shallow geologic framework of the Louisiana-Mississippi shelf. Work was done by Alpine Ocean Seismic Survey, Inc., onboard the M/V Blue Streak 8 and was coordinated with geophysical surveys done by the USGS onboard the R/V Gyre and the R/V Carancahua in 1981 and R/V Acadiana in 1987.  This appendix contains the description sheets (.pdf) and interpreted classification profiles (.txt) from the 42 cores that were collected in Federal waters east of the Chandeleur Islands.  No information was found for core CI-87-03-Curlew.

Purpose: These cores were part of a study to map the shallow geologic framework of the Louisiana-Mississippi shelf and provide a sand resource inventory.

Supplemental_Information: The Blue Streak 8 is a 130-ft leg class vessel owned by Blue Streak Marine of Belle Chase, LA.

Time_Period_of_Content:

Time_Period_Information:

Range_of_Dates/Times:

Beginning_Date: 1987

Ending_Date: 1987

Currentness_Reference: Data collection interval

Status:

Progress: Complete

Maintenance_and_Update_Frequency: None planned

Spatial_Domain:

Bounding_Coordinates:

West_Bounding_Coordinate: -89.320

East_Bounding_Coordinate: -88.524

North_Bounding_Coordinate: 30.123

South_Bounding_Coordinate: 29.340

Keywords:

Theme:

Theme_Keyword_Thesaurus: None

Theme_Keyword: CI-87

Theme_Keyword: Vibracore

Theme_Keyword: Geologic Framework

Theme_Keyword: Sand Resource Inventory

Theme_Keyword: M/V Blue Streak

Theme_Keyword: Alpine Ocean Seismic Survey, Inc.

Theme_Keyword: Louisiana Department of Natural Resources

Place:

Place_Keyword_Thesaurus: None

Place_Keyword: Louisiana

Place_Keyword: Mississippi

Place_Keyword: Chandeleur Islands

Place_Keyword: Chandeleur Sound

Place_Keyword: Louisiana-Mississippi shelf

Place_Keyword: Gulf of Mexico

Access_Constraints: None. These data are held in the public domain.

Use_Constraints:

The U.S. Geological Survey requests to be acknowledged as originator of the data in future products or derivative research.

Point_of_Contact:

Contact_Information:

Contact_Person_Primary:

Contact_Person: James G. Flocks

Contact_Organization: U.S. Geological Survey

Contact_Position: Geologist

Contact_Address:

Address_Type: mailing and physical

Address: 600 4th Street South

City: St. Petersburg

State_or_Province: FL

Postal_Code: 33701

Country: USA

Contact_Voice_Telephone: (727) 803-8747, ext. 3012

Contact_Electronic_Mail_Address: jflocks@usgs.gov

Data_Set_Credit:

Vibracores were collected by Alpine Ocean Seismic Survey, Inc. under contracts with the Louisiana Department of Natural Resources and the USGS.  Funding came from the Bureau of Land Management (BLM), Minerals Management Service (MMS), LGS, and the USGS.

Spatial_Reference_Information:

Horizontal_Coordinate_System_Definition:

Geographic:

Latitude_Resolution: 0.0000027

Longitude_Resolution: 0.0000027

Geographic_Coordinate_Units: decimal degrees

Geodetic_Model:

Horizontal_Datum_Name: WGS84

Ellipsoid_Name: WGS84

Semi-major_Axis: 6378137

Denominator_of_Flattening_Ratio: 298.257

Entity_and_Attribute_Information:

Overview_Description:

Entity_and_Attribute_Overview:

GIS file: a point shapefile of vibracore locations is available.

Data_Quality_Information:

Attribute_Accuracy:

Attribute_Accuracy_Report:

The validity or accuracy of the navigation system depended on equipment and operating condition variables. Visual inspection of the location data did not show any major anomalies.

Logical_Consistency_Report:

This data set is from one cruise with consistent instrument calibrations.

Completeness_Report:

Positional_Accuracy:

Horizontal_Positional_Accuracy:

Horizontal_Positional_Accuracy_Report:

The position of the vessel was recorded in latitude and longitude using a Syledis (SYstem LEgere pour mesure le DIStance) navigation system. This system uses pre-existing shore stations in a range-range mode with accuracy of plus/minus 5 m.  The position of each core was corrected for the offset between the coring tower and the antennae location.

Vertical_Positional_Accuracy:

Vertical_Positional_Accuracy_Report:

Water depths were taken from the vessel’s digital fathometer before jacking up.  No tide corrections were made.

Lineage:

Process_Step: Vibracore Collection

Process_Description:

Vibracores were collected with an Alpine Model 271 Vibracorer.  This system is capable of obtaining cores up to 40 ft below the ocean bottom.  The support tower was a 45-ft-long aluminum H-beam supported by four foot-pads and stiff legs which were attached to a cross bar 12 ft above the base of the tower.  The tower served as a sliding guide for the air-driven vibrator which drove the attached core pipe into the ocean bottom sediments.  The sediments were retained in a clear 3 5/8-inch ID plastic liner inserted in the metal core pipe.  Two 20-ft sections were spliced together in order to get the 40-ft core barrels.

When initial vibratory attempts failed to penetrate the full 40 ft, a jetting technique was employed.  A new liner was inserted inside the coring pipe and the vibracore rig placed on the ocean bottom close to the initial coring location.  High pressure water was pumped via a 2-inch hose down through the core pipe, washing away the sediment and allowing the pipe to penetrate to the depth where the first run encountered refusal.  The water was then turned off and the air to the vibrator turned on, thus continuing the coring process.

Process_Step: Core Description

Process_Description:

Each core was split lengthwise into two equal halves.  One half was visually described using standard sediment logging methods and sampled at 0.3-m (1.0-ft) intervals for textural analysis.  Additional samples were taken from the top and bottom of sand-rich intervals greater than approximately 0.6-m (2.0-ft) thick to allow for more effective textural classification of sedimentary units. Description sheets were scanned and saved as PDF files. The hardcopy description sheets were archived at the USGS FISC-St. Petersburg, FL.  The remaining half of each core was cut into 1.0-m (3.28-ft) intervals, photographed in detail, wrapped in plastic sleeves, and archived at the University of New Orleans (UNO) Department of Geology and Geophysics Chevron core warehouse in New Orleans, LA.  All cores were lost in August, 2005, during flooding events associated with Hurricane Katrina.

Spatial_Data_Organization_Information:

Indirect_Spatial_Reference:

Distribution_Information:

Distributor:

Contact_Information:

Contact_Person_Primary:

Contact_Person: James G. Flocks

Contact_Organization: U.S. Geological Survey

Contact_Position: Geologist

Contact_Address:

Address_Type: mailing and physical

Address: 600 4th Street South

City: St. Petersburg

State_or_Province: FL

Postal_Code: 33701

Country: USA

Contact_Voice_Telephone: (727) 803-8747, ext. 3012

Contact_Electronic_Mail_Address: jflocks@usgs.gov

Contact_Instructions:

Resource_Description: Distribution_Liability:

Although these data have been processed successfully on a computer system at the U.S. Geological Survey, no warranty expressed or implied is made regarding the display or utility of the data on any other system, or for general or scientific purposes, nor shall the act of distribution imply any such warranty. The U.S. Geological Survey shall not be held liable for improper or incorrect use of the data described and (or) contained herein. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not constitute or imply its endorsement, recommendation, or favoring by the United States Government or any agency thereof.

Standard_Order_Process:

Digital_Form:

Digital_Transfer_Information:

Format_Name:

Format_Information_Content:

File_Decompression_Technique:

Transfer_Size:

Digital_Transfer_Option:

Offline_Option:

Offline_Media:

Recording_Format:

Compatibility_Information: UNIX, Linux, DOS, Macintosh

Digital_Form:

Digital_Transfer_Information:

Format_Name:

Format_Information_Content:

File_Decompression_Technique:

Transfer_Size:

Digital_Transfer_Option:

Online_Option:

Computer_Contact_Information:

Network_Address:

Network_Resource_Name:

Fees:

Ordering_Instructions:

Technical_Prerequisites:

Metadata_Reference_Information:

Metadata_Date: 20090108

Metadata_Contact:

Contact_Information:

Contact_Person_Primary:

Contact_Person: Jordan M. Sanford

Contact_Organization: U.S. Geological Survey

Contact_Position: Physical Scientist

Contact_Address:

Address_Type: mailing and physical

Address: 600 4th Street South

City: St. Petersburg

State_or_Province: FL

Postal_Code: 33701

Country: USA

Contact_Voice_Telephone: (727) 803-8747, ext. 3025

Contact_Electronic_Mail_Address: jsanford@usgs.gov

Metadata_Standard_Name: Content Standard for Digital Geospatial Metadata

Metadata_Standard_Version: FGDC-STD-001-1998