U.S. GEOLOGICAL SURVEY DIGITAL DATA SERIES DDS-18-A

                     National Geochemical Data Base: 
                National Uranium Resource Evaluation Data
                   for the Conterminous United States


                            SOFTWARE PROBLEMS


       RAM MEMORY LIMITATIONS

       You may encounter problems running the GSSEARCH or MAPPER software
       due to your computer's memory limitations.  GSSEARCH requires about
       500KB of RAM to run, but will use expanded or extended memory if
       available, and also uses overlays to improve its efficiency.  The
       browse record display selection loads as many records as it can into
       the available RAM (as many as fifteen at a time).  If sufficient
       memory is not available, fewer records will be loaded for the browse
       display.  GSSEARCH also allocates memory from RAM for record output
       tags, so you may have insufficient memory to output a large number
       of records.  MAPPER uses about 540KB.  It also allocates small
       amounts of memory for saving the screen behind pop-up menus.
       Additionally, GSMENU uses about 38KB, and each submenu uses about
       another 1KB.

       If memory problems occur, you should remove all unnecessary drivers
       and TSR programs from system memory.  You can determine your
       system's memory availability and usage by running DOS command MEM.
       If you have DOS 6.0 or above, you can use the DOS command MemMaker
       to configure your computer's memory more efficiently.

       If you continue to have problems, you can run GSSEARCH and MAPPER
       without going through GSMENU.  Simply use NURE48GS.BAT to run
       GSSEARCH, and use NURE48MA.BAT to run MAPPER.  These batch files
       were copied to your hard disk into the NURE48 directory during
       the installation process.


       DISC MEMORY LIMITATIONS 

       GSSEARCH requires about 1MB of hard disk space for temporary files.
       Additional space may be required for retrievals.  You may also run
       out of disk space if you are trying to output a large number of
       records from GSSEARCH.  If you are only interested in certain fields
       in each record, use the "Selected Fields" option in the GSSEARCH
       output to reduce the size of each output record.

       MAPPER requires about 400KB of hard disk space for each map file
       saved.  Map files may be moved from the \NURE48 directory to an
       alternate hard disk, but the alternate path must be added to the
       MAPPER command line if these map files are to be accessible.  See
       the section below on adding alternate paths for mapper for
       information on how to do this.


       GSSEARCH SPEED IMPROVEMENTS

       Because GSSEARCH uses overlays to reduce RAM requirements, if your
       PC has insufficient memory GSSEARCH may operate slowly, since it
       has to copy the program overlay segments from the CD-ROM disk into
       RAM as they are needed.  You may be able to greatly speed up the
       operation of the GSSEARCH software by copying it to your hard disk.
       This may be done in the installation process.  If it is done there,
       the GSMENU data file for the main menu (NURE48A.MNU) will
       automatically be edited to accommodate the change.

       If you have already installed the software, and you decide that you
       wish to run GSSEARCH from your hard disk, you may simply reinstall
       the software.  You may also copy GSSEARCH.EXE, GSSEARCH.HLP, and
       GSSEARCH.MSG from the CD-ROM SOFTWARE directory to the NURE48
       directory on your hard disk.  Then edit NURE48A.MNU to change line
       eighteen from

         romltr:\SOFTWARE\GSSEARCH.EXE,GSSEARCH,romltr:\NURE48\NURE48,romltr,

       to

         hrdltr:\NURE48\GSSEARCH.EXE,GSSEARCH,romltr:\NURE48\NURE48,romltr,

       where  

         romltr is the CD-ROM drive letter,
         hrdltr is the hard disk drive letter.

       You may also edit NURE48GS.BAT from

         romltr:\SOFTWARE\GSSEARCH romltr:\NURE48\NURE48 romltr

       to

         hrdltr:\NURE48\GSSEARCH romltr:\NURE48\NURE48 romltr

       See the note below regarding editing of these files.


       GSSEARCH BROWSE FORMAT CHANGES

       You may alter one or more of the GSSEARCH browse formats.  To do so
       you must copy the NURE48.CFG file from the NURE48 directory of the
       CD-ROM to the NURE48 directory of your hard disk.  You may then
       edit the browse format or formats following instructions in
       GSSEARCH.DOC, which is in the \SOFTWARE directory of the CD-ROM.
       You must then edit NURE48A.MNU and NURE48GS.BAT to direct GSSEARCH
       to use the new CFG file.  Edit NURE48A.MNU to change line eighteen
       from

         romltr:\SOFTWARE\GSSEARCH.EXE,GSSEARCH,romltr:\NURE48\NURE48,romltr,

       to

         hrdltr:\NURE48\GSSEARCH.EXE,GSSEARCH,hrdltr:\NURE48\NURE48,romltr,

       where  

         romltr is the CD-ROM drive letter,
         hrdltr is the hard disk drive letter.

       You may also edit NURE48GS.BAT from

         romltr:\SOFTWARE\GSSEARCH romltr:\NURE48\NURE48 romltr

       to

         hrdltr:\NURE48\GSSEARCH hrdltr:\NURE48\NURE48 romltr

       See the note below regarding editing of these files.

        
       MAPPER SPEED IMPROVEMENTS

       You may speed up the loading of the map file by the MAPPER software
       by saving a built map to your hard disk.  This requires about 400KB
       of disk space.  See \DOCFILES\GETSTART.DOC and \MAPPER\MAPPER.DOC 
       for further information on this procedure.

       If you are generating many zoomed map images, you may speed up the 
       generation of the images from the digital data files by creating
       a directory on your hard disk and copying the contents of the 
       \MAPPER directory on the CD-ROM to the new directory.  This requires
       about 28MB of disk space.  The \MAPPER\TUTORIAL or \MAPPER\SOFTWARE
       subdirectories do not need to be copied.


       ADDING ALTERNATE PATHS FOR MAPPER

       The MAPPER map file selection software first looks for map files in
       the directory from which it was started, in this case the \NURE48
       directory on your hard disk.  If any are found they are listed in
       the file menu.  If none are found it automatically looks in the
       directory where MAPPER.EXE is located, in this case the \MAPPER
       directory on the CD-ROM drive.  It then looks in any alternate paths
       which may be specified in the MAPPER command line.  These alternate
       paths may be accessed by pressing <Esc> at the file selection menu.
       MAPPER will find only the GRF files that are in the directory from 
       which it was started.  

       You may add alternate paths to the MAPPER command line to allow the
       software to look for map files in locations other than the \NURE48
       directory of your hard disk and the \MAPPER directory of the CD-ROM.
       To do so you must edit NURE48A.MNU (and/or NURE48MA.BAT).  To edit
       NURE48A.MNU, change line nineteen from

           3 2 3

         to 

           3 3 3

       This tells GSMENU that there are three arguments in the following 
       menu data line instead of the original two.  Then edit line twenty 
       from 

         romltr:\MAPPER\MAPPER.EXE,MAPPER,
         
       to 

         romltr:\MAPPER\MAPPER.EXE,MAPPER,alt_path,

       where  

         romltr is the CD-ROM drive letter
         alt_path is the added alternate path (including drive letter) 
           for map files.

       For each added path, increment the middle number of line nineteen 
       by one.  Make sure there is a comma between each path, and at the 
       end of the last path.  

       You may also edit NURE48MA.BAT from

         romltr:\MAPPER\MAPPER

       to

         romltr:\MAPPER\MAPPER alt_path

       Additional alternate paths may be added in the same manner.


       NOTE:  All editing of the GSMENU menu data file must be done using 
       an ASCII editor, or edited with a word processor and saved as ASCII,
       with no control characters except carriage return (ASCII 13) and
       line feed (ASCII 10).  See \DOSMENU\GSMENU.DOC for further 
       information on the use of the GSMENU software.