Using 'linefix.c': 
 
     The program 'linefix' edits vectors (or line work) used by 
programs 'mapper' and 'collage'.  Program 'linefix' works with 
binary files made by program 'reorder' and outputs the type of 
ASCCI file used by program 'reorder'.  Program 'linefix' will 
automatcally run 'reorder' if you request to do so when exiting 
the program. 
 
     The process is to first build one or more ASCII files 
defining the line work you will be mapping.  All points must be 
in decimal degrees with latitude first.  North latitude and east 
longitude are positive.  The system maintains an accuracy of a 4 
byte floating point number.  Therefore, even though six places 
after the decimal (nearest centimeter) will be printed in the 
ASCII output files the most information that is really there is 
usually five places after the decimal point (nearest meter) of 
accuracy avaliable.  The ASCII line file begins each input line 
with and attribute which can range from - to + 2 billion.  The 
attribute is followed by a series of alternating latitudes and 
longitudes.  The last longitude is marked by two slashes with no 
spaces between the number and the salshes.  Marking the last 
entry of a line in this way removes the requirement to count 
points in each line when editing a file with a word processor.  
The type of the file is 'RAW'.  An example of a '.raw' file 
follows: 
 
FILE:  'aaa.raw' 
 
 
     0 
     32  -97  32  -95  30  -95  30  -97  32  -97// 
     1 
     32 -100  32  -98  30  -98  30 -100  32 -100// 
     2 
     29 -102  29 -100  27 -100  27 -102  29 -102// 
     3 
     29 -105  29 -103  27 -103  27 -105// 
      
 
     Running reorder on this file will create three binary files 
'aaa.bin', 'aaa.hdr' and 'aaa.atr'.  To run reorder simply type: 
 
     reorder aaa p 
 
     To use 'mapper' to view the map you will need a '.map' file 
to describe the map for plotting.  The following is an example of

such a file: 
 
 
FILE:  'aaa.map' 
 
     p   2.220   30.0   -100.0   10.0 
     begin_color 
        black    =   0   0   0 
        d_grey   =  46  46  46 
        l_grey   = 128 128 128 
        white    = 255 255 255 
         buff     = 105  90  75 
        l_buff   = 130 111  93 
        brown    =  96  28  14 
        red      = 255   0   0 
        orange   = 255 128   0 
        yellow   = 160 160   0 
        green    =   0 200   0 
        d_green  =   0 120   0 
        vd_green =   0  72   0 
        blue     =   0   0 200 
        d_blue   =   0  20  60 
        magenta  = 255   0 255 
     end_color 
      
     menu_background = d_grey 
              text = l_grey 
           highlight = white 
          background = buff 
           graticule = l_buff 
             lat/lon = d_grey 
               black = black 
      
     begin_vector 
        test_lines = 2  ON 
           aaa 100 0 red 
           xxx 110 0 green 
     end_vector 


     The important part of this file is the last 5 lines where
the vectors (lines) are defined.  For the purpose of editing only
the file names are of importance but the other information must
be there for 'linefix' to correctly identify the vectors you wish
to work with.  Also, program 'mapper' will find the lines in any
directory you tell it to look, but program 'linefix' requires all
data to be in the current working directory.  So copy all 'bin',
'hdr' and 'atr' files you will be using into a work directory
before you begin editing.

     Since you will only have one file of linework (aaa) if you
are following this example the file 'xxx' will not exist when you
run 'linefix' the first time.  If you add a line or change one of
the lines in 'aaa' you can save the results as 'xxx' when you
exit the program.  You will then have two files to work with. 
The program is self explanitory but a list of just what can be
done may help.



--------------------------------------------------------------
                                                 Menu Level
---------------------------------------------- ---------------
Function                                       Main Sub  Sub 2
---------------------------------------------- ---- ---- -----
Locate points on map                             L
Edit a line                                      e
Add a line                                       a
Move a point                                     e    m
Turn cursor off during point moving              e    m    c
Turn cursor on during point moving               e    m    c
Add point on either side of a point              e    a
Delete a point                                   e    d
Delete a line                                    e    D
   note:  all delelted lines are placed
          in file 'linefix.raw' which can
          be renamed and used as a new file
          of selected lines.
Save an edited line                              e    s
Exit without saving line                         e    x
                                                 a    x
Zoom                                             z
                                                 e    z
Reset to original map                            r
                                                 e    r
Replot to last zoom setting                      l
                                                 e    l
Replot screen at same setting                    e    R
--------------------------------------------------------------




Mapper System Overview:         ÚÄÄÄÄ<ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ<ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  
          ÚÄÄÄÄÄÄÄÄÄÄÄ¿         ³     ÚÄÄÄÄÄÄÄÄÄÄÄ¿                    ³  
    ÚÄÄÄÄ<³ASCII.raw *³         ÃÄÄÄÄ>³ASCII.lab *³>¿                  ³
    ³     ÀÄÄÄÄÄÄÄÄÄÄÄÙ         ³     ÀÄÄÄÄÄÄÄÄÄÄÄÙ ³                  ³
    ³                           ³                   ³                  ³
    ÃÄ>ÚÄ< FILTER               ³  ÚÄ< MAKEBLB <ÄÄÄÄÙ     ÚÄÄÄÄÄÄÄÄÄÄÄ¿³
    ³  ³                        ³  ³                  ÚÄÄ<³ASCII.map *³³ 
    ³  ³  ÚÄÄÄÄÄÄÄÄÄ¿           ³  ³  ÉÍÍÍÍÍÍÍÍÍÍ»    ³   ÀÄÄÄÄÄÄÄÄÄÄÄÙ³
    ³  ÃÄ>³ASCII.raw³>¿         ³  ÀÄ>ºbinary.blbº>ÄÂÄ´                ³
    ³  ³  ÀÄÄÄÄÄÄÄÄÄÙ ³         ³     ÈÍÍÍÍÍÍÍÍÍÍ¼  ³ ³                ³
    ³  ³ÚÄÄÄÄÄÄ<ÄÄÄÄÄÄÙ         ³                   ³ ³                ³
 ÚÄÄÁ>ÄÁÁ> REORDER ÄÄÄ¿         ÀÄÄÄÄ< MAKELAB <ÄÄÄÄÙ ³                ³
 ³       ÉÍÍÍÍÍÍÍÍÍÍ» ³                               ÃÄÄÄÄ<ÄÄÄÄÄÄÄÄÄ¿ ³
 ³     Ú<ºbinary.hdrº<´            ÚÄÄÄÄÄÄÄ<ÄÄÄÄÄÄÄÄÄÄÙ              ³ ³
 ³     Ã<ºbinary.binº<´<ÄÄÄ¿       ³                                 ³ ³
 ³     Ã<ºbinary.atrº<Ù    ³       ³                                 ³ ³
 ³     ³ ÈÍÍÍÍÍÍÍÍÍÍ¼      ³       ³                   ÉÍÍÍÍÍÍÍÍÍÍ»  ³ ³
 ³     ÀÄÄ>ÄÄÄÂÄÄÄÄÄÄÄÄ>ÄÄÄÄÄÄÄÂÄ>ÄÁÄÄÄ> MAPPER >ÄÄÂÄÄ>ºbinary.mprº>ÄÙ ³
 ³            ³            ³   ³                   ³   ÈÍÍÍÍÍÍÍÍÍÍ¼    ³   
 ³  MAKERAW <ÄÁÄ> LINEFIX >Ù   ³                   ÃÄÄÄÄÄÄÄÄÄ>ÄÄÄÄÄÄÄÄÄÙ
 ³     ³             ³         ³                   ³                       
 ³     ³ ÚÄÄÄÄÄÄÄÄÄ¿ ³         ³     ÉÍÍÍÍÍÍÍÍÍÍ»  ³              
 ³     À>³ASCII.raw³<Ù         ÃÄÄÄÄ<ºbinary.xmpº<ÄÙ              
 ³       ÀÄÄÄÄÄÄÄÄÄÙ           ³     ÈÍÍÍÍÍÍÍÍÍÍ¼                          
 À<ÄÄÄÄÄÄÄÄÄÄÄÙ                ³                        ÉÍÍÍÍÍÍÍÍÍÍÍÍ»
                               ÀÄÄÄÄÄÄÄ> XMP2TGA8 >ÄÄÄÄ>ºbinary.tga**º
                                                        ÈÍÍÍÍÍÍÍÍÍÍÍÍ¼   
 ÄÄÄ ASCII files
 ÍÍÍ binary files
  *  Main ASCII input files.
 **  Output is one of 4 standard Targa file formats.

Line Work:


ASCII.raw Files:

     The left side of the diagram is the part of the system which controls the
line work.  Programs are in upper case and files have ASCII or binary followed
by a file type.  The line work input file is an ASCII file with decimal degree
latitudes and longitudes.  North and east are positive.  West and south are
negative.  The file type is '.raw'  and the format is as follows:

     0
     32.0  -97.0  32.0  -95.0  30.0  -95.0  30.0  -97.0  32.0  -97.0//
     1
     32.0 -100.0  32.0  -98.0  30.0  -98.0  30.0 -100.0  32.0 -100.0//
     2
     29.0 -102.0  29.0 -100.0  27.0 -100.0  27.0 -102.0  29.0 -102.0//
     3
     29.0 -105.0  29.0 -103.0  27.0 -103.0  27.0 -105.0//

     The first number is an attribute which may or may not have meaning.  It
is stored as a signed 8 byte integer number so size is not a problem.  This is
followed by as many lat/lon pairs as are necessary to define the line.  The
double slash marks the end of the line.  This makes editing with a word
processor easy because it removes the necessity of counting points, which is
difficult for long segments.  The number of lines in a file is limited to
10,000 or less.


Program FILTER:

     The '.raw' files can be run through program 'filter' to remove points for
drawing at smaller scales.  If the pixel size on the screen is 5 kilometers it
makes no sense to plot points 2 meters apart.  The same pixel will just be
replotted 2500 times.  Filter keeps the end points of the line and insures
that other points are at least the minimum distance apart.  The output is also
a raw file.

     To run filter the command line is:

         filter  <filename> <scale>

         e.g.

          filter stream 2

     The filename has no type (program filter knows that it must be a '.raw'
file).  The scale is as follows:

         scale   minimum distance  suffix

          1     100.00 kilometers     0
          2      10.00 kilometers     A
          3       1.00 kilometers     B
          4       0.10 kilometers     C
          5       0.01 kilometers     D

     The above example will use the file 'stream.raw' to create 'streama.raw'
in which all points will be at least 10 kilometers apart (except for the last
two points).


Program REORDER:

     To use the data in a reasonable interactive way these ASCII flat files
must be converted to a set of binary files.  Reorder does this by using the
following command line:

     reorder <filename> <option>

     e.g.

     reorder streama r

     The options are as follows:

          c -- just count segments in file (do not process)
          R -- reorder file and make binary file without dupes
          r -- reorder file and make binary file
          p -- same as 'r' but not in order



Program MAKERAW:

     Program 'mapper' is the main recipient of these files but there are two
other programs which use them.  Programs 'makeraw' and 'linefix' which can use
these files.  Program 'makeraw' makes raw files from the binary and attribute
files and can be used to extract a small geographic subset from a large area
file.

     makeraw <infile> <outfile> [MaxLat MinLat MaxLon MinLon]

     example:

     makeraw l:\demo\road1a d:\mydir\m_road1a  45.0 35.0 -100.0 -124.0

     The above command will extract from the binary file of main highways
(filtered to 10 km.) on the 1:2,000,000 DLG CD-ROM disc and make a file on my
disk bounded by 35 and 45 north latitude and 100 and 124 west longitude.


Program LINEFIX:

     Program 'linefix' is an editor which allows you to pull in a work file
and any number of background files,  change the work file in any way you wish
and output new or updated '.raw' files or binary files.  If you delete and
lines they are placed in file 'linefix.raw'  so the program can be used to
select a small number of lines from a large file, line by line.  The program
is self explanatory and runs from '.map' files which control the program just
as they control program 'mapper'.  The major differences are (1) only line
work is used and (2) all files must be in the current working directory.  Copy
all file you wish to work with into a directory for editing, edit them then
move them out.  It is not a good idea to work on original files if no copy
exists.  Also if you add lines save the file and restart the program before
trying to change them.  As with any editor, frequent saves will prevent lost
work.

                          Using 'linefix.c': 
 
          The program 'linefix' edits vectors (or line work) used by 
     programs 'mapper' and 'collage'.  Program 'linefix' works with 
     binary files made by program 'reorder' and outputs the type of 
     ASCCI file used by program 'reorder'.  Program 'linefix' will 
     automatcally run 'reorder' if you request to do so when exiting 
     the program. 
      
          The process is to first build one or more ASCII files 
     defining the line work you will be mapping.  All points must be 
     in decimal degrees with latitude first.  North latitude and east 
     longitude are positive.  The system maintains an accuracy of a 4 
     byte floating point number.  Therefore, even though six places 
     after the decimal (nearest centimeter) will be printed in the 
     ASCII output files the most information that is really there is 
     usually five places after the decimal point (nearest meter) of 
     accuracy avaliable.  The ASCII line file begins each input line 
     with and attribute which can range from - to + 2 billion.  The 
     attribute is followed by a series of alternating latitudes and 
     longitudes.  The last longitude is marked by two slashes with no 
     spaces between the number and the salshes.  Marking the last 
     entry of a line in this way removes the requirement to count 
     points in each line when editing a file with a word processor.  
     The type of the file is 'RAW'.  An example of a '.raw' file 
     follows: 
      
     FILE:  'aaa.raw' 
      
          0 
          32  -97  32  -95  30  -95  30  -97  32  -97// 
          1 
          32 -100  32  -98  30  -98  30 -100  32 -100// 
          2 
          29 -102  29 -100  27 -100  27 -102  29 -102// 
          3 
          29 -105  29 -103  27 -103  27 -105// 
           
      
          Running reorder on this file will create three binary files 
     'aaa.bin', 'aaa.hdr' and 'aaa.atr'.  To run reorder simply type: 
      
          reorder aaa p 
      
          To use 'mapper' to view the map you will need a '.map' file 
     to describe the map for plotting.  The following is an example of
     
     such a file: 
      
      
     FILE:  'aaa.map' 
      
          p   2.220   30.0   -100.0   10.0 
          begin_color 
             black    =   0   0   0 
             d_grey   =  46  46  46 
             l_grey   = 128 128 128 
             white    = 255 255 255 
              buff     = 105  90  75 
             l_buff   = 130 111  93 
             brown    =  96  28  14 
             red      = 255   0   0 
             orange   = 255 128   0 
             yellow   = 160 160   0 
             green    =   0 200   0 
             d_green  =   0 120   0 
             vd_green =   0  72   0 
             blue     =   0   0 200 
             d_blue   =   0  20  60 
             magenta  = 255   0 255 
          end_color 
           
          menu_background = d_grey 
                   text = l_grey 
                highlight = white 
               background = buff 
                graticule = l_buff 
                  lat/lon = d_grey 
                    black = black 
           
          begin_vector 
             test_lines = 2  ON 
                aaa 100 0 red 
                xxx 110 0 green 
          end_vector 
     
     
          The important part of this file is the last 5 lines where
     the vectors (lines) are defined.  For the purpose of editing only
     the file names are of importance but the other information must
     be there for 'linefix' to correctly identify the vectors you wish
     to work with.  Also, program 'mapper' will find the lines in any
     directory you tell it to look, but program 'linefix' requires all
     data to be in the current working directory.  So copy all 'bin',
     'hdr' and 'atr' files you will be using into a work directory
     before you begin editing.
     
          Since you will only have one file of linework (aaa) if you
     are following this example the file 'xxx' will not exist when you
     run 'linefix' the first time.  If you add a line or change one of
     the lines in 'aaa' you can save the results as 'xxx' when you
     exit the program.  You will then have two files to work with. 
     The program is self explanitory but a list of just what can be
     done may help.
     
     
     
     --------------------------------------------------------------
                                                      Menu Level
     ---------------------------------------------- ---------------
     Function                                       Main Sub  Sub 2
     ---------------------------------------------- ---- ---- -----
     Locate points on map                             L
     Edit a line                                      e
     Add a line                                       a
     Move a point                                     e    m
     Turn cursor off during point moving              e    m    c
     Turn cursor on during point moving               e    m    c
     Add point on either side of a point              e    a
     Delete a point                                   e    d
     Delete a line                                    e    D
        note:  all delelted lines are placed
               in file 'linefix.raw' which can
               be renamed and used as a new file
               of selected lines.
     Save an edited line                              e    s
     Exit without saving line                         e    x
                                                      a    x
     Zoom                                             z
                                                      e    z
     Reset to original map                            r
                                                      e    r
     Replot to last zoom setting                      l
                                                      e    l
     Replot screen at same setting                    e    R
     --------------------------------------------------------------
     


The Control File:

     If line work is all that you will be displaying you are very nearly done
at this point.  All you need now is a file which tells program 'mapper' what
lines to plot, which colors to use, where the map is located and the scale and
projection of the map.  The control file is of type '.map' which is one of the
things program 'mapper' searches for when it starts.  The following file is
the minimum you can have and it is set to plot the lower 48 states on your
screen and only the files streama, streamb and stream will be plotted.


     p  8.0   38.0   -95.75   10.0
     begin_color                
          black    =   0   0   0
          d_grey   =  46  46  46
          l_grey   = 128 128 128
          white    = 255 255 255
          buff     = 105  90  75
          l_buff   = 130 111  93
          brown    =  96  28  14
          red      = 255   0   0
          orange   = 255 128   0
          yellow   = 160 160   0
          green    =   0 200   0
          d_green  =   0 120   0
          vd_green =   0  72   0
          blue     =  30  60 255
          d_blue   =   0  20  60
          magenta  = 255   0 255
     end_color                  
     menu_background = d_grey     
                text = l_grey     
           highlight = white      
          background = buff       
           graticule = l_buff     
             lat/lon = d_grey     
               black = black      
     begin_vector 
       geology = 3 ON
         streama  10.0 3.0 d_blue
         streamb   3.0 0.3 d_blue
         stream    0.3 0.0 d_blue
     end_vector



     The following is the complete format of a map file.  All comments (which
are not part of the file) are in [square brackets].

p  0.5   18.3  -66.44  10.0  

     [  The 1st line has a character and 4 numbers             ]
     [  char is projection                                     ]
     [     p = plate carree or x-y projection (recomended)     ]
     [     a = Albers equal area                               ]
     [     s = polarstereographic                              ]
     [     S = sinusoidal                                      ]
     [     m = Mercator                                        ]
     [  0.5 is pixel size of center pixel in kilometers        ]
     [ 18.3 is latitude of center pixel                        ]
     [-66.4 is longitude of center pixel                       ]
     [ 10.0 is a number of no use but it must be there         ]



begin_color                  [  You can define up to 16 VGA    ]
     black    =   0   0   0  [  (or EGA) colors here for use   ]
     d_grey   =  46  46  46  [  in line work.  The format is   ]
     l_grey   = 128 128 128  [  a color name, =, then a red,   ]
     white    = 255 255 255  [  green, and blue color value.   ]
     buff     = 105  90  75  [                                 ]
     l_buff   = 130 111  93  [                                 ]
     brown    =  96  28  14  [                                 ]
     red      = 255   0   0  [                                 ]
     orange   = 255 128   0  [                                 ]
     yellow   = 160 160   0  [                                 ]
     green    =   0 200   0  [                                 ]
     d_green  =   0 120   0  [                                 ]
     vd_green =   0  72   0  [                                 ]
     blue     =  30  60 255  [                                 ]
     d_blue   =   0  20  60  [                                 ]
     magenta  = 255   0 255  [                                 ]
end_color                    [  this must be here to mark end  ]


menu_background = d_grey     [  The pull down menu can be made ]
           text = l_grey     [  any color but something must   ]
      highlight = white      [  be given for each item.        ]
     background = buff       [  This is the blank screen color.]
      graticule = l_buff     [                                 ]
        lat/lon = d_grey     [                                 ]
          black = black      [                                 ]

begin_vector 
  geology = 2 ON
    east_geo  3.0 0.0 d_grey 
    west_geo  3.0 0.0 d_grey

[ A list of the vector filenames must be given with group      ]
[ names.  You can have up to 25 groups and up to 25 vectors in ]
[ a group.  The group names are used while the program is      ]
[ running to identify vectors for plotting or labeling.  Each  ]
[ group name is followed by '=', the number of vectors in the  ]
[ group and the word 'ON' of 'OFF' to tell wheter to plot it   ]
[ the first time through.                                      ]
[                                                              ]
[ Each vector name is followed by a maximum pixel size, a      ]
[ minimum pixel size and the color (from above) to plot the    ]
[ vector.  In this example we are going to color in geologic   ]
[ formations so the first vectors (lines) to be plotted are    ]
[ the polygons defining the formations on the map.  They will  ]
[ be plotted when the pixel size is less than 3 km.            ]

     fillin_IHS = 1
          geology.blb      3.0   0.0
  2  0.66 234  0.90 Thqdp
  3  0.61 234  0.80 Tgp
  1  0.83 254  0.33 TKgqm
  4  0.81 234  0.50 Thdap
end

[ This entry tells how to fill in the polygons.  It must be    ]
[ located after the polygons are plotted and before other lines]
[ are plotted.  The file 'geology.blb' was made from a file    ]
[ called 'geology.lab' which was made using this program and   ]
[ the /l option, and the cursor mode 'P' option, e.g.          ]
[     mapper /l geology.lab                                    ]
[ then running 'makeblb geology' on the '.lab' file to make    ]
[ the .blb file.                                               ]
[                                                              ]
[  The numbers give the pixel sizes to plot the fill.  The next]
[  1 to 240 lines are polygon fill values (used with the 'P'   ]
[  option in cursor mode) followed by intensity (0-1.0), hue   ]
[ (1-255) and saturation (0-1.0).  Use the cursor mode 'E'     ]
[ option to set and chose these colors.                        ]


Program MAPPER:

     Program mapper will now draw maps on the screen as well as output several
files which can be reused by program mapper or processed into Targa files and
sent out to other printing devices.  To run the program just type 'mapper' but
several command line options are available.  What the program does depends on
what the command file tells it to do and what types of data files and hardware
are available to it.

     command line options:

        /e = EGA
        /v = VGA 640x480x16 colors
        /s = VGA 320x200x256 colors
        /y = Extended VGA 640x400x256 colors
        /x = Extended VGA 640x480x256 colors

        /l [path][file_name].[file_type] = output '.LAB' file of points
        /o [path][file_name].[file_type] = output run information file
        /a [path][file_name] = automatic map load on start
        /p [program_name] = passes control to program from point (S)earch
        /r creates a '.MPR' file with ranges of data for all files then stops
        /h help -- prints this message
        /grid [sample rate] = outputs '.lab' entry for a grid of points

        Any path name for data search can by added also, e.g. D:\DATA or
        \MAPPER\DATA\MAP

     cursor mode options:

        All Maps
           (G)raph Data Points   -- see 'graph.c' for instructions
           (L)ocate Vectors      -- labels line if '*.atr' file exists
           (S)earch for nearest point -- find and labels points if available
           e(x)it to picture      -- lists '*.lbl' files of points if any
        Color Filled Maps All Modes
           (k)ey                 -- plots a small key on right side of screen
           (K)ey                 -- plots a large key on right side of screen
           (N)ame all            -- prints polygon name at all label points
           (P)aint area          -- fills a polygon with color entered and
                                    makes entry in '*.lab' file if /l
                                    option on
        Color Filled Maps Modes 'X', 'Y' and 'S' Only
           (n)ame 1              -- labels polygon at cursor location
           (p)aint mark          -- makes entry in '*.lab' file if /l
                                    option on
           (R)emove lines        -- removes polygon boundaries
           (E)dit colors         -- changes map color and gives color info
           (C)olor table output  -- outputs color table
           (f)lash               -- makes color flash white then return
           (D)arker              -- makes map fill colors darker but not lines
           (B)righter            -- makes map fill colors brighter but not
                                    lines

Program XMP2TGA8:

     The output format of the map images is a binary file which contains, not
only the map image, but all of the control information used by program
'mapper' to draw the map.  The format is not standard and is dificult to
export to other devices.  Program 'xmp2tga8' corrects this problem.


   Program 'xmp2tga8' reads a map output file from program 'mapper'
   of type '.xmp' and outputs a targa file of type '.tga'.  To run
   the program enter command line:

        xmp2tga8 [infile] <option>

        option:
             /p -- run-length packed file (default)
             /f -- full resolution file (every pixel of map image)
            /24 -- 24-bit real color
            /32 -- 32-bit real color