U.S. GEOLOGICAL SURVEY OPEN FILE REPORT 94-255

       The Southern Lake Michigan Coastal Erosion Study CD-ROM


      By  C.F. Polloni1, C.L. Brown2, D.W. Folger1, D.S. Foster1,
                           and A.L. Brill3



                  Display software by Russell A. Ambroziak4
                  Documentation by Christine A. Cook4



	1U.S. Geological Survey, Woods Hole, MA 02543
	2U.S. Forest Service, Jacksonville, OR 97530
	3Duke University, Durham, NC 27708
	4U.S. Geological Survey, Reston, VA 22092


                                 Klein system


       Sidescan-sonar  data were collected with a 100-kHz Klein  system, 
       which  had  a  range of 100 m on each side.   Survey  lines  were 
       approximately 125 m apart to achieve about 30 percent data  over-
       lap between adjacent lines. The analog data  were printed on a 
       Klein 531 three-channel  sidescan-sonar recorder.   Some of the
       original data were digitized at sea or in the lab using a QMIPS
       computer system. The latest  version of the U.S.  Geological 
       Survey's  sidescan-sonar data  acquisition  system  is described
       by  Danforth and others  (1991).   In  order  to transfer the acoustic
       data to spatially correct sonar  images, a considerable amount of
       computer processing  was required using methods similar to those
       described by Chavez (1986).  Once processing of data from individual
       cruise tracks in the mosaic areas was completed, the images were
       projected and  mosaicked  to form the composite images which are
       viewed  in full resolution when selected for viewing either from a map
       or individually using the program IMVIS which is provided for use on
       the  CD-ROM.   The  application of sidescan-sonar  data  for  the 
       purpose  of geologic interpretation was described by Johnson  and 
       Helferty (1990).


                          End of text; press the Escape key to continue.