| Column name | Column definition |
| --- | --- |
|  | (Note: all column names ending in "J" originated from J. Dyni's original tops file) |
| ID | Software-calculated identifier |
| USGSIDJ | Unique ID assigned by staff geologist |
| CMPNYPROJJ | Name of the company or agency that drilled the borehole |
| NAMEJ | Name of the borehole assigned by the company or agency that drilled it |
| EASTWESTJ | Distance in feet measured east or west from section line |
| NORSOUJ | Distance in feet measured north or south from section line |
| QQJ | Quarter-quarter section |
| RANGEJ | Range |
| SECJ | Section |
| TWPJ | Township |
| LATDDJ | Latitude in decimal degrees, North American Datum 1927, original record |
| LONGDDJ | Longitude in decimal degrees, North American Datum 1927, original record |
| LOCSRCJ | Source of the borehole location, usually from the Fischer assay file, geophysical log, lithologic log, or survey |
| COUNTYJ | Name of county in Colorado |
| ELEVFTJ | A borehole reference elevation, such as ground surface, rotary bushing, or rotary table, from which down hole depths were measured |
| COREDINTVJ | Depths, in feet, of the sequence that was cored in the borehole |
| ELEVSRCJ | Source of elevation, usually from the Fischer assay file, geophysical log, lithologic log, topo or survey |
| TOTDEPTFTJ | Total depth of the borehole, in feet |
| QUADJ | Name of 7.5-minute USGS topographic map, borehole may or may not be shown on map |
| ARCHIVEDJ | Core archived yes or no |
| YRDRILLEDJ | Year that the borehole was drilled |
| LOCCOREJ | Physical location of the core from core hole, for example, USGS Core Research Center |
| SHOWNMAPJ | Indicates whether the actual borehole location is shown on the topographic map |
| LITHFTJ | Top and bottom borehole depths, in feet, of sequence of core or rotary cuttings for which a lithologic log was prepared |
| PHOTOFTJ | Top and bottom borehole depths, in feet, of photographic record of drill core |
| ELECFTJ | Top and bottom depths, in feet, of electric log of borehole |
| GAMMAFTJ | Top and bottom depths, in feet, of gamma ray log of borehole |
| DENSFTJ | Top and bottom depths, in feet, of density log of borehole |
| SONICFTJ | Top and bottom depths, in feet, of sonic log of borehole |
| NEUTRONFTJ | Top and bottom depths, in feet, of neutron log of borehole |
| CALIPERFTJ | Top and bottom depths, in feet, of caliper log of borehole |
| RQDFTJ | Top and bottom borehole depths, in feet, of rock quality data log |
| TEMPFTJ | Top and bottom depths, in feet, of temperature log of borehole |
| OTHERLOGSJ | Top and bottom depths, in feet, of other geophysical logs |
| FISCHASSYJ | Top and bottom depths, in feet, of sequence analyzed by Fischer assays |
| LABJ | Name of laboratory where Fischer assays were performed |
| ALUMINAFTJ | Top and bottom depths, in feet, of sequence analyzed for alumina |
| NUMBASSYSJ | Number of Fischer assays that were made |
| USBMNUMBRJ | A number assigned to the report of Fischer assays made by the former U.S. Bureau of Mines |
| LOCATNOTEJ | Additional information, commonly used where there is a problem with the location |
| NAHCOLTFTJ | Top and bottom depths, in feet, of sequence analyzed for nahcolite |
| XRDFTJ | Top and bottom depths, in feet, of X-ray diffraction analyses made on samples from the borehole |
| ELEVNOTEJ | Additional information, commonly used where there is a problem with the elevation |
| MISCNOTEJ | Miscellaneous information, such as publications related to the borehole, and other data |
| REVISDATEJ | Date of last revision for original borehole data |
| NAME | Name of the borehole assigned by the company or agency that drilled it |
| TRSEC | Township, range, and section |
| EASTWEST | Distance in feet measured east or west from section line |
| NORSOU | Distance in feet measured north or south from section line |
| LATDD | Latitude in decimal degrees, North American Datum 1927, software-calculated, this report (2009) |
| LONGDD | Longitude in decimal degrees, North American Datum 1927, software-calculated, this report (2009) |
| ELEVFT | A borehole reference elevation, such as ground surface, rotary bushing, or rotary table, from which down hole depths were measured |
| CHDH | Core hole or drill hole |
| ELEVDATUM | Elevation, in feet, for various reference surfaces including Kelly bushing, ground level, topographic map, and rotary table |
| USGSID | Unique ID assigned by staff geologist |
| JD76 | Depth to top of Bed 76, in feet |
| JD74 | Depth to top of Bed 74, in feet |
| JD72 | Depth to top of Bed 72, in feet |
| JDTPPORCTF | Depth to top of Porcupine Creek tuff, in feet |
| JDBSPORCTF | Depth to base of Porcupine Creek tuff, in feet |
| JD70 | Depth to top of Bed 70, in feet |
| JD68 | Depth to top of Bed 68, in feet |
| JD67 | Depth to top of Bed 67, in feet |
| JD66 | Depth to top of Bed 67, in feet |
| JD64 | Depth to top of Bed 64, in feet |
| JD62 | Depth to top of Bed 62, in feet |
| JD60 | Depth to top of Bed 60, in feet |
| JD58 | Depth to top of Bed 58, in feet |
| JD56 | Depth to top of Bed 56, in feet |
| JD54 | Depth to top of Bed 54, in feet |
| JD52 | Depth to top of Bed 52, in feet |
| JD50 | Depth to top of Bed 50, in feet |
| JD48 | Depth to top of Bed 48, in feet |
| JD46 | Depth to top of Bed 46, in feet |
| JD44BIG3 | Depth to top of Bed 44 of Big 3 oil shale beds, in feet |
| JD42BIG3 | Depth to top of Bed 42 of Big 3 oil shale beds, in feet |
| JD40BIG3 | Depth to top of Bed 40 of Big 3 oil shale beds, in feet |
| JD39 | Depth to top of Bed 39, in feet |
| JD38STLWTR | Depth to top of Stillwater zone, in feet |
| JD37 | Depth to top of Bed 37, in feet |
| JD36A | Depth to top of Bed 36A, in feet |
| JD36 | Depth to top of Bed 36, in feet |
| JD34 | Depth to top of Bed 36, in feet |
| JD32FRSENR | Depth to top of Bed 32 of the Four Senators, in feet |
| JD30 | Depth to top of Bed 30 of the Four Senators, in feet |
| JD28FRSENR | Depth to top of Bed 28 of the Four Senators, in feet |
| JD26 | Depth to top of Bed 26 of the Four Senators, in feet |
| JD25 | Depth to top of Bed 25, in feet |
| JD24 | Depth to top of Bed 24, in feet |
| JD22 | Depth to top of Bed 22, in feet |
| JD21 | Depth to top of Bed 21, in feet |
| JD20 | Depth to top of Bed 20, in feet |
| JD18 | Depth to top of Bed 18, in feet |
| JD16 | Depth to top of Bed 16, in feet |
| JD14 | Depth to top of Bed 14, in feet |
| OTPUPWAVY | Depth to top of Upper Wavy, in feet |
| OBSUPWAVY | Depth to base of Upper Wavy, in feet |
| JD12 | Depth to top of Bed 12, in feet |
| JD10 | Depth to top of Bed 10, in feet |
| JD08 | Depth to top of Bed 8, in feet |
| JD06 | Depth to top of Bed 6, in feet |
| JD04 | Depth to top of Bed 4, in feet |
| JD02 | Depth to top of Bed 2, in feet |
| JDAGROOV | Depth to top of A Groove, in feet |
| JDMAHOGZN | Depth to top of Mahogany Zone, in feet (space holder, not used in this assessment) |
| OMAHOGZN | Depth to top of Mahogany Zone, in feet |
| JDTPMAHOG | Depth to top of Mahogany Bed (Donnell, USGS), in feet (space holder, not used in this assessment) |
| OMAHOG | Depth to top of Mahogany Bed (Johnson, USGS), in feet |
| JDBGROOV | Depth to top of B Groove, in feet |
| JDR6 | Depth to top of R6 Zone, in feet |
| JDL5 | Depth to top of L5 Zone, in feet |
| JDR5 | Depth to top of R5 Zone, in feet |
| JDL4 | Depth to top of L4 Zone, in feet |
| JDR4 | Depth to top of R4 Zone, in feet |
| JDL3 | Depth to top of L3 Zone, in feet |
| JDR3 | Depth to top of R3 Zone, in feet |
| JDL2 | Depth to top of L2 Zone, in feet |
| R2 | Depth to top of R2 Zone, in feet |
| L1 | Depth to top of L1 Zone, in feet |
| R1 | Depth to top of R1 Zone, in feet |
| CLASTCR1TP | Depth to top of clastic wedge in R-1 zone, in feet |
| CLASTCR1BS | Depth to base of clastic wedge in R-1 zone, in feet |
| L0 | Depth to top of L0 Zone, in feet |
| R0 | Depth to top of R0 Zone, in feet |
| LPBS | Depth to base of Long Point, in feet |
| BMARKRTP | Depth to top of B Marker, in feet |
| BMARKRBS | Depth to base of B Marker, in feet(space holder, not used in this assessment) |
| CMARKRTP | Depth to top of C Marker, in feet |
| CMARKRBS | Depth to base of C Marker, in feet(space holder, not used in this assessment) |
| DMARKRTP | Depth to top of D Marker, in feet |
| DMARKRBS | Depth to base of D Marker, in feet(space holder, not used in this assessment) |
| FMARKR | Depth to top of F Marker, in feet |
| IMARKR | Depth to top of I Marker, in feet |
| TOPILES | Depth to top of Iles, in feet |
| TOPKMV | Depth to top of Kmv, in feet |
| TOPRLNS | Depth to top of Rollins, in feet |
| TOPCSGT | Depth to top of Castlegate, in feet |
| MHG2BGRV | Thickness of interval from the Mahogany bed to B Groove, in feet |
| MHGZN2BGRV | Thickness of interval from the Mahogany zone to B Groove, in feet |
| BGRV2R6 | Thickness of interval from B Groove to the R6 zone, in feet |
| R62L5 | Thickness of interval from R6 to the L5 zone, in feet |
| L52R5 | Thickness of interval from L5 to the R5 zone, in feet |
| R52L4 | Thickness of interval from R5 to the L4 zone, in feet |
| L42R4 | Thickness of interval from L4 to the R4 zone, in feet |
| R42L3 | Thickness of interval from R4 to the L3 zone, in feet |
| L32R3 | Thickness of interval from L3 to the R3 zone, in feet |
| R32L2 | Thickness of interval from R3 to the L2 zone, in feet |
| L22R2 | Thickness of interval from L2 to the R2 zone, in feet |
| R22L1 | Thickness of interval from R2 to the L1 zone, in feet |
| L12R1 | Thickness of interval from L1 to the R1 zone, in feet |
| R12L0 | Thickness of interval from R1 to the L0 zone, in feet |
| L02R0 | Thickness of interval from L0 to the R0 zone, in feet |
| R02LPBS | Thickness of interval from R0 to the Long Point base, in feet |
| AGRV2MHGZN | Thickness of interval from A Groove to the Mahogany zone, in feet |
| B442AGRV | Thickness of interval from Bed 44 to A Groove, in feet |
| MGBS2R5 | Thickness of interval from the Mahogany zone base to the R5 zone, in feet |
| R52LPBS | Thickness of interval from R5 to the Long Point base, in feet |
| JD762JD44 | Thickness of interval from bed 76 to bed 44, in feet |