# FINAL REPORT

on

Data Acquisition and Processing

for the

# Airborne Magnetic Survey

# of

# Death Valley, California

on behalf of the

# United States Geological Survey

# Brian Schacht   P. Geoph.

# Ottawa, Ontario, Canada

# March, 2001

# TABLE OF CONTENTS

# 1.	INTRODUCTION	3

2.	TECHNICAL SPECIFICATIONS	4

  - SURVEY LOCATION	4

  - FLIGHT SPECIFICATIONS	4

2.3	TOLERANCES	4

2.4	SURVEY EQUIPMENT	5

3.	PERSONNEL	6

4.	SURVEY OPERATIONS	7

4.1	GENERAL	7

4.2	DIURNAL CONDITIONS	7

4.3	GENERAL WEATHER CONDITIONS	7

4.4	QUALITY CONTROL AND FIELD PROCESSING	7

5.	CALIBRATION AND TEST RESULTS	8

5.1	GPS BASE STATION	8

5.2	MAGNETIC LAG TEST	8

5.3	GPS LAG / ACCURACY TEST	9

5.4	FIGURE OF MERIT	11

  - ALTIMETER CALIBRATION	11

6.	FINAL MAGNETIC DATA PROCESSING	12

6.1	NOISE EDITING	12

6.2	NOISE FILTERING	12

6.3	DIURNAL SUBTRACTION	12

6.4	IGRF CORRECTION	12

6.5	UPWARD/DOWNWARD CONTINUATION	13

6.6	LEVELLING	13

6.7	GRIDDING	13

6.8	GRID LEVELLING	13

7.	DELIVERABLES	14

  - MAPS		14

7.2	REPORT	14

7.3	DIGITAL ARCHIVES	14

APPENDIX:	DIGITAL ARCHIVE FORMAT DESCRIPTION			 15

# 1.	INTRODUCTION

An aeromagnetic survey was flown over Death Valley, California, as well as three conjoined areas within western Nevada.  The flying was completed between December 5, 2000, and January 14, 2001, by Fugro Airborne Surveys on behalf of the United States Geological Survey (see figure 1).  A 1:100,000 scale contour map and digital grid of the total magnetic field were produced, as well as a digital grid of radar altimeter (ground clearance) data.

2.	TECHNICAL SPECIFICATIONS							  4

This section describes in detail the guidelines followed throughout the performance of the project; tolerances and instruments are also presented here.

  - SURVEY LOCATION

The area is bounded by the following co-ordinates (WGS84 UTM and degrees X 1,000,000):

500000.00  3979126.00    35572348  -117000000

552103.00  3979126.00    35571847  -116252002

512687.00  4039215.00    36295343  -116513001

512646.00  4066946.00    36445341  -116513002

470243.00  4066988.00    36445340  -117200003

470163.00  4043879.00    36322342  -117200002

500000.00  4043828.00    36322345  -117000000

# 2.2	FLIGHT SPECIFICATIONS

Traverse Line Direction			E - W

Traverse Line Spacing			400 m

Control Line Direction			N - S

Control Line Spacing			approximately 7,500 m

Terrain Clearance				117-1217 m+ - see section 2.3 - “Flying Height”

Line kilometers				8135.82 (5055.5 miles)

Average Sampling Interval		7.5 m

# 2.3	TOLERANCES

Lines (or segments of lines crossing two control lines, or segments of control lines crossing several lines) were re-flown when any of the following tolerances were exceeded:

# Navigation

- Nominal line spacing must not be exceeded by more than 50% for a distance of more than 3.2 km.

Flight Height

- In order to maintain similar elevations at all traverse and control line intersections, even when climbing or descending steeply, the Fugro ACCUDRAPE system utilizes a pre-planned digital drape surface which the onboard computer compares with the GPS xyz to feed corrections to the pilot.

- Deviations from the pre-planned drape elevation must not exceed 100 m.  The precipitous mountains flanking the survey necessitated a pre-planned drape surface with ground clearance exceeding 1217 m (4000’) over the valley (the radar altimeter maximum is 1217 m).  Less than 1% of the data could be flown below 183 m (600’).

Magnetic Diurnal

- Deviations must not be greater than 2 nT from a 2 minute chord.  The ground station magnetometer operated during all data acquisition.

# Airborne Magnetometer Noise

- “Maneuver” noise must not exceed an envelope of ±0.1 nT over more than 10% of any line.  This was monitored on the analog chart with a fourth difference and a high-pass filter.

- A standard Figure of Merit must be less than 1.5 nT.

- Heading errors must be within 1 nT between reciprocal headings.

# 2.4	SURVEY EQUIPMENT

# Table 2.4.a lists major characteristics of the fixed-wing survey aircraft.

| Registration | Endurance | Engines | Manufacturer | Type | No. of Seats | Average Speed |
| --- | --- | --- | --- | --- | --- | --- |
| C-FZLK | 6.5 hours | 1 Turbine | Cessna | Caravan 208 | 3 | 75 m/sec |

## Table 2.4.a  Survey Aircraft

Table 2.4.b lists the geophysical equipment installed in C-FZLK throughout the survey.

| Equipment | Manufacturer | Model | Type |
| --- | --- | --- | --- |
| Data Acquisition System | Fugro Airborne Surveys | GeoDAS | Pentium computer based, real-time, data synchronization and recording |
| Magnetometer | Scintrex | CS-2 | Cesium Vapour,10 Hz Sampling, 0.005 nT Sensitivity,0.001 nT Resolution |
| Compensator | RMS | AADC | 27 Term |
| Digital Backup | Iomega | Zip Drive | 100 Mb removable hard drive |
| Analogue Recorder | RMS | GR-33a-1 | Dot Matrix |
| Radar Altimeter | TRT | AVH-8 | 10 Hz Sampling, Accuracy ±2% |
| Barometric Altimeter | Rosemount | 1241M | 10 Hz Sampling, Accuracy ±5 m |
| Omnistar Receiver | Trimble |  | Real-time differential GPS correction |
| GPS Receiver | Sercel | NR103 | 10 Channel |
| Video Camera | Panasonic | WVC 1302 | Colour |
| Video Cassette Recorder | Panasonic | AG2400 | NTSC |

# Table 2.4.b  Airborne Geophysical Equipment

# Table 2.4.c lists the components of the ground-based reference station.

| Equipment | Manufacturer | Model | Type |
| --- | --- | --- | --- |
| Magnetometer | Scintrex | CS-2 | Cesium Vapour, 2 Hz Sampling, 0.005 nT Sensitivity, 0.01 nT Resolution |
| GPS Receiver | Sercel | NR-103 | 10 Channel |

# Table 2.4.c  Ground Reference Station

The ground magnetometer was mounted in a magnetically quiet area; its clock was synchronized with the GPS time signal.  The GPS data logger records all of the raw range data stream.  The Trajecto differential correction software matches the output from the airborne GPS system and the ground GPS system during the data reduction process.

# Table 2.4.d lists the equipment and software used to perform the field processing.

| Equipment | Manufacturer | Model | Type |
| --- | --- | --- | --- |
| PC | Dell | Inspiron 7500 | 800 MHz Pentium |
| Printer | HP | HP950C | A4 Colour |
| Data Processing Software | Fugro Airborne Surveys | Gmaps | DOS & Windows |
| Image Processing Software | ERMapper | Version 5.5 | Windows 95/98 |
| GPS Processing Software | Sercel | Trajecto | DOS |

# Table 2.4.d  Field Processing System

3.	PERSONNEL

| NAME | TITLE | PROJECT POSITION |
| --- | --- | --- |
| Robb, Jeff | Aircraft Maintenance Engineer | Aircraft Maintenance |
| Lamirande, Ken | Electronics Technician | Electronics Operator |
| Reed, Travis | Electronics Technician | Electronics Operator |
| Lyall, Ron | Operations Manager | Processor, Logistics |
| Williston, Mark | Pilot | Survey Pilot |
| Thomas, Jeff | Pilot | Survey Pilot |

### Table 3   Field Project Personnel

4.	SURVEY OPERATIONS

  - GENERAL

The production phase of the project began in Bishop, California, on December 5th , 2000, and the final production flight was made on January 14th, 2001.  The Comfort Inn provided crew accommodation and space for the field processing office.

  - DIURNAL CONDITIONS

Magnetic diurnal variation was exceptionally quiet.  Deviations never reached the specification limit.

  - GENERAL WEATHER CONDITIONS

Weather conditions were frequently unfavourable for survey flying due to high turbulence or cloud cover in the mountains.  Ten days were lost.

  - QUALITY CONTROL AND FIELD PROCESSING

- To check the data for adherence to contract specifications and move the data closer to the final stage, the following procedures were followed for each flight (details in section 6):

- downloading and verification of aircraft data;

- downloading and verification of GPS and magnetic base station data;

- post-processing of GPS data using SERCEL TRAJECTOGRAPHY software;

- merging of navigation data with geophysical data including transformation of coordinates from WGS84 latitude/longitude to UTM x, y coordinates in the local spheroid;

- creation of flight path plots and evaluation of compliance with contract specifications;

- spike and null value location and removal from the magnetic and altimeter data;

- computing of a drape surface quality control field for evaluation of compliance with the contract specifications;

- computing of magnetic noise channel for evaluation of data quality and compliance with contract specifications;

- evaluation of diurnal data quality, and compliance with contract specifications;

- correction of magnetic data for I.G.R.F. gradient;

- noise filtering of magnetic and altimeter fields;

- correction of magnetic field for altitude deviations;

- backing-up of all field data.

At regular intervals, the corrected magnetic data were levelled and gridded for quality inspection including real-time shade enhancement.

5.	CALIBRATION AND TEST RESULTS

5.1	GPS BASE STATION

To apply post-flight differential GPS corrections to the survey data, a GPS base station was installed near the crew’s hotel.  The location of the GPS base station antenna was determined by averaging positions over a 24 hour period.  The location was 37o 22’ 17.28” N latitude, 118o 22’ 8.46” W longitude, elevation 1,255 m, on the WGS spheroid.

  - MAGNETIC LAG TEST

The camera on-board the aircraft records its position, A, relative to the ground, at time t0.  In fact the sensor will arrive over A at time t1 (>t0).  Furthermore, because of electronic delays, the reading at time t1 will not be recorded until time t2 (>t1).  The difference t2-t0 represents the lag between the actual aircraft position and the x y position tied to the magnetic reading on disk.  A lag test was performed by flying the aircraft at survey altitude in opposite directions over a sharp magnetic feature.  The position of the magnetic feature was referenced to a visible feature recorded by the video system, in this case a bridge, which was the anomaly source.  By superimposing a plot of the east-west anomaly over the west-east anomaly, the video-picked position of the bridge can be transposed onto its counterpart; and one-half the difference between the two video-picked positions equals the magnetic system lag.  The lag was 0.7 seconds, or 7 magnetic samples, for aircraft C-FZLK.  These values were used to correct for magnetic system lag throughout the survey.

5.3	GPS LAG / ACCURACY.TEST

A cloverleaf flown over the established co-ordinates of the Canadian Geological Survey test site was used to measure the lag in the GPS positioning, with regard to the video camera position.  A value of 0.2 seconds resulted in a best fit with the video position.  Once the lag is applied (as in figure 5.3) the cloverleaf intersection is used to test the accuracy of the GPS positioning.

| Aircraft: |  | Cessna Caravan |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Registration: |  | C-FZLK |  |  |  |
| Date: |  | November 25, 2000 |  |  |  |
| Location: |  | Bourget, Ontario, Canada |  |  |  |
| Altitude: |  | 400 ft mean terrain clearance |  |  |  |
| DIRECTION | FIDUCIAL CLOSEST TO TARGET | OFFSET FROM TARGET DUE TO PILOT ERROR | Line # on Video |  |  |
|  | (from video) | (estimate in metres & direction) |  |  |  |
| South | 66216.56 | 0 | Line 10 |  |  |
| West | 66326.92 | 3 N | Line 11 |  |  |
| North | 66413.50 | 20 E | Line 12 |  |  |
| East | 66506.22 | 5 N | Line 13 |  |  |
| South | 66595.44 | 5 W | Line 14 |  |  |
| West | 66709.76 | 5 N | Line 15 |  |  |
| East | 66884.10 | 0 | Line 17 |  |  |
| North | 66992.44 | 15 E | Line 18 |  |  |

TABLE 5.3 GPS LAG / ACCURACY TEST

5.4	FIGURE OF MERIT (FOM)

The figure of merit is the measurement of the ability of the compensation system to remove the effects of aircraft maneuvers from the total field data.  During the FOM test the aircraft is flown into a quiet magnetic area and put through a series of pitches (±5o), rolls (±10o) and yaws (±5o) to examine the noise remaining in the signal after the 27 term automatic compensation algorithm has been applied to the data.

|  | Figure of Merit |  |  |  |
| --- | --- | --- | --- | --- |
| Aircraft: |  | Cessna Caravan |  |  |
| Registration: |  | C-FZLK |  |  |
| Magnetometer: |  | Cesium vapor, stinger mounted |  |  |
| Sampling Rate: |  | 10 Hz |  |  |
| Date: |  | December 2, 2000 |  |  |
| Location: |  | Bishop, California |  |  |
| HEADING | MANOEUVER | VALUE (nT) | HEADING |  |
|  |  |  | TOTAL (nT) |  |
| NORTH | PITCH | 0.18 |  |  |
|  | ROLL | 0.08 |  |  |
|  | YAW | 0.06 | 0.32 |  |
| EAST | PITCH | 0.12 |  |  |
|  | ROLL | 0.07 |  |  |
|  | YAW | 0.08 | 0.27 |  |
| SOUTH | PITCH | 0.08 |  |  |
|  | ROLL | 0.06 |  |  |
|  | YAW | 0.04 | 0.18 |  |
| WEST | PITCH | 0.08 |  |  |
|  | ROLL | 0.06 |  |  |
|  | YAW | 0.06 | 0.20 |  |
|  |  | FOM VALUE | 0.97 | nT |
| AVERAGE MANEUVER NOISE ( FOM / 12 ) |  |  | 0.08 | nT |

# Table 5.4   C-FZLK Figure of Merit

# 5.5	ALTIMETER CALIBRATION

# On November 24, 2000, the radar, barometric, and GPS altimeters were compared by flying at terrain clearances of 200’, 300’, 400’, 500’, 600’, 800’, and 1000’ over a flat portion of the Ottawa river.  The results reconfirmed that all altimeters aboard C-FZLK are functioning normally.

# 6.	FINAL DATA PROCESSING

Final data reduction was undertaken at the Fugro Airborne Surveys processing center in Ottawa, Canada between January and February, 2001.  In general, final processing consisted of the following operations:

- final levelling of the total field magnetic data;

- image and 1:100,000 scale map analysis of the total field and levelling compensations by a geophysicist for any levelling, positioning, or gridding errors;

- final gridding and micro-levelling;

- imaging and plotting of magnetic field;

- gridding of radar altimeter data

- archiving of final data.

The final projection was the Universal Transverse Mercator using the NAD83 (WGS84) spheroid, with a false easting of 500,000 m, false northing of 0 m, scale factor of 0.9996 and central meridian of 117o West.

Further details of the magnetic processing are provided below.

# 6.1	Noise Editing

An automatic editing routine, employing 4th differences of the magnetic field, removed nulls and spikes down to the noise level, and located abrupt level shifts.

6.2	Noise Filtering

We filtered  all data in the frequency domain with a cutoff 0.061 (wavelengths per sample interval) rolloff 0.030 (wavelengths per sample interval).  This filter approaches 100% removal of anomalies of wavelength 99 metres (13.2 samples x average speed of 7.5 metres/sample) or less. It approaches 0% removal of anomalies of wavelength 163 metres (21.7 samples x average speed of 7.5 metres/sample) or more.  This filter should have no effect on any real, geological-source anomalies; or even the narrowest anomaly from cultural sources on the ground surface.  The minimum ground clearance is about 150 metres (rarely encountered) and the minimum wavelength produced at 150 metres is roughly 2 x 150 = 300 metres.  Thus all real wavelengths are a safe distance from the 163 metre limit of the filter.

# 6.3	Diurnal Subtraction

A test was made to verify the effectiveness of diurnal subtraction: Long period diurnal variations were subtracted from the air data, as they are more likely to correlate, and the residual magnetic field was leveled.  As no improvement was noted in the required levelling compensations, diurnal subtraction was not employed.

6.4	IGRF Correction

The IGRF regional value was calculated using the 1995 model updated to the mid-survey date (2001.0) using the corrected GPS elevations.  Using the actual elevations for IGRF correction has the added benefit of correcting for the magnetic effect of altitude variations within the Earth’s primary field.  Corrections for vertical movements within the secondary magnetic field induced by the Earth’s crust is discussed in the following section, 6.5.

  - Upward/Downward Continuation

As the terrain clearance drops, the vertical magnetic gradients can become very high; and even minor deviations from the prescribed drape surface may produce significant changes in the measured magnetic field.  The Taylor Expansion applies the required upward and downward continuations to the magnetic field to simulate measurements from the prescribed altitude.  The resulting magnetic field profiles were input to the levelling process.

  - Levelling

The lines (traverse lines) and tie-lines (control lines) of an aeromagnetic survey form a network, and the points where they cross are called intersections.  At each intersection the magnetic values should be identical.  In practice they differ as a result of:

-	time variations of the magnetic field;

-	heading effects;

-	altitude differences;

-	position errors;

-	cultural or instrument noise.

In the levelling process, it is assumed that most of the required level adjustments will vary smoothly along each line or tie-line.  The network of line minus tie-line differences at the intersections is analyzed to produce a matrix of misclosures.  These misclosures were reduced to zero through an iterative process of tilting the profile baselines and moving the intersection locations.  Compensation values applied at adjacent tie-lines were not allowed to differ by more than 5 nT.  Intersection movements were restricted to a maximum of 4 samples (about 30 metres).  These maximums were very rarely required.  None of the 1,121 intersections needed manual corrections.

# 6.7	Gridding

Gridding was done by the Akima method, using data from all lines and tie-lines.  A gridding interval of 1/3 the line spacing was used (133 m).

# 6.8	Grid Levelling

The final stage of levelling consisted of applying a grid-levelling routine to the gridded data to remove small residual errors that are not properly removed by conventional levelling of the line data

7.	DELIVERABLES

7.1	MAPS

Two copies of the magnetic field contour map are presented at 1:100,000 scale with UTM registration plus screened flight path, in black and white, on mylar.

7.2	REPORT

This report covers data acquisition and processing, and is provided in two hard copies plus a digital archive in Microsoft Word format.

7.3	DIGITAL ARCHIVES

Files:		raw and final processed profile data, and final magnetic and radar altitude grids;

Format:	The ASCII  format is used for profiles, and Geosoft binary format is used for grids.  A full format description is included in the appendix .

Media:	CD-ROM.

Copies:	two

We trust this survey will assist your mapping program; and we remain available for questions at any time.

Respectfully Submitted,

Brian Schacht   P. Geoph.

APPENDIX

DIGITAL ARCHIVE FORMAT DESCRIPTOR

DIGITAL ARCHIVE DESCRIPTION OF PROFILE DATA

DEATH VALLEY, CALIFORNIA

Digital Archive is Ascii.

Ascii filename: california.profile

250 bytes I 10 format

1-10 Line number X 100 + part number

11-20 Flight number

21-30 Latitude   NAD27 (decimal degrees)

31-40 Longitude

41-50 UTM metres NAD27 (CM 117 degrees west)

51-60 UTM metres

61-70 Latitude   WGS84 (decimal degrees)

71-80 Longitude

81-90 UTM metres WGS84 (CM 117 degrees west)

91-100 UTM metres

101-110 Fiducial (seconds UTC X 10 increments by 1)

111-120 Date (ddmmyy)

121-130 Radar (m X 100)

131-140 Baro  (m X 100)

141-150 GPS elevation (m X 100)

151-160 Diurnal (.001 nT)

161-170 Raw Magnetics (.001 nT) edited, lag applied.

171-180 Filtered Magnetics (.001 nT)

181-190 Filtered Magnetics - I.G.R.F. (.001 nT)

191-200 I.G.R.F. (2000.9)

201-210 Differential Up/Down corr. Magnetics (.001 nT)

211-220 Levelled Magnetics (.001 nT)

221-230 Final Magnetics (.001 nT)

231-240 Compensation (.001 nT) from TL levelling

241-250 Compensation (.001 nT) from micro levelling

Fugro Airborne Survey's direction codes are as follows:

1: Northbound

2: Eastbound

3: Southbound

4: Westbound

The archive file contains the following lines:

ARCHIVE FILE: california.archive

------------

LINE-ID   DIR FST-FID LST-FID TAPE   BLOCK    REC  SAMPLES

----------- ---   (X10)   (X10) ----   -----    ---  -------

10101   3   56599   56919    1         1     1    3201

10201   1   57317   57633    1      3202     1    3161

10301   3   57805   58137    1      6363     1    3321

10401   1   58333   58680    1      9684     1    3471

10501   3   58827   59175    1     13155     1    3481

10601   1   59378   59711    1     16636     1    3331

10701   3   59874   60216    1     19967     1    3421

10801   1   60372   60692    1     23388     1    3201

10901   3   60863   61204    1     26589     1    3411

11001   1   61368   61712    1     30000     1    3441

11101   3   62470   62805    1     33441     1    3351

11201   1   62997   63320    1     36792     1    3231

11301   3   63483   63825    1     40023     1    3421

11401   1   63981   64318    1     43444     1    3371

11501   3   64468   64806    1     46815     1    3381

11601   1   64970   65316    1     50196     1    3461

11701   3   65484   65815    1     53657     1    3311

11801   1   65965   66298    1     56968     1    3331

11901   3   66858   67223    1     60299     1    3651

12001   1   67385   67721    1     63950     1    3361

12101   3   68016   68355    1     67311     1    3391

12201   1   68523   68861    1     70702     1    3381

12301   3   69021   69365    1     74083     1    3441

12401   1   69526   69861    1     77524     1    3351

12501   3   70035   70369    1     80875     1    3341

12601   1   70565   70909    1     84216     1    3441

12701   3   71675   72011    1     87657     1    3361

12801   1   72199   72524    1     91018     1    3251

12901   3   72693   73040    1     94269     1    3471

13001   1   73211   73544    1     97740     1    3331

13101   3   56169   56532    1    101071     1    3631

13201   1   56725   57075    1    104702     1    3501

13301   3   57228   57588    1    108203     1    3601

13401   1   57777   58118    1    111804     1    3411

13501   3   58255   58611    1    115215     1    3561

13601   1   58801   59151    1    118776     1    3501

13701   3   59635   59979    1    122277     1    3441

13801   1   60138   60497    1    125718     1    3591

13901   3   60669   61010    1    129309     1    3411

14001   1   61179   61569    1    132720     1    3901

14101   3   61732   62077    1    136621     1    3451

14201   1   62245   62605    1    140072     1    3601

14301   3   62807   63140    1    143673     1    3331

14401   1   63306   63689    1    147004     1    3831

14501   3   63857   64203    1    150835     1    3461

14601   1   64359   64717    1    154296     1    3581

14701   3   65016   65361    1    157877     1    3451

14801   1   65532   65897    1    161328     1    3651

14901   3   66057   66398    1    164979     1    3411

15001   1   66571   66924    1    168390     1    3531

15101   3   67093   67445    1    171921     1    3521

15201   1   67618   67966    1    175442     1    3481

15301   3   68150   68498    1    178923     1    3481

15401   1   68680   69033    1    182404     1    3531

15501   1   70448   70802    1    185935     1    3541

15601   3   69954   70306    1    189476     1    3521

15701   1   69284   69641    1    192997     1    3571

15801   3   68659   69020    1    196568     1    3611

15901   3   67470   67845    1    200179     1    3751

16001   1   68003   68355    1    203930     1    3521

16101   1   66832   67178    1    207451     1    3461

16201   3   66257   66622    1    210912     1    3651

16301   1   65616   65982    1    214563     1    3661

16401   3   65087   65446    1    218224     1    3591

16501   1   64482   64838    1    221815     1    3561

16601   3   63886   64249    1    225376     1    3631

16701   1   63255   63621    1    229007     1    3661

16801   3   62699   63070    1    232668     1    3711

16901   1   86129   86437    1    236379     1    3081

17001   3   85574   85871    1    239460     1    2971

17101   1   85136   85452    1    242431     1    3161

17201   3   84704   85001    1    245592     1    2971

17301   1   67006   67373    1    248563     1    3671

17401   3   66479   66822    1    252234     1    3431

17501   3   83850   85044    1    255665     1   11941

17601   1   85554   86676    1    267606     1   11221

17701   3   57132   58313    1    278827     1   11811

17801   1   58501   59921    1    290638     1   14201

17901   3   60085   60930    1    304839     1    8451

17902   3   61160   61525    1    313290     1    3651

18001   1   61709   63120    1    316941     1   14111

18101   3   63550   64737    1    331052     1   11871

18201   1   64931   66355    1    342923     1   14241

18301   3   73525   74634    1    357164     1   11091

18402   1   75260   76170    1    368255     1    9101

18403   1   72995   73260    1    377356     1    2651

18501   3   76316   76990    1    380007     1    6741

18502   3   77280   77614    1    386748     1    3341

18503   1   73350   73500    1    390089     1    1501

18601   1   77781   78960    1    391590     1   11791

18701   3   79099   80190    1    403381     1   10911

18801   1   80345   81526    1    414292     1   11811

18901   3   81898   82997    1    426103     1   10991

19001   1   83388   84554    1    437094     1   11661

19101   3   56456   57802    1    448755     1   13461

19201   1   57955   59215    1    462216     1   12601

19301   3   59411   60810    1    474817     1   13991

19401   1   61151   62424    1    488808     1   12731

19502   3   57921   59149    1    501539     1   12281

19602   3   63306   64511    1    513820     1   12051

19701   3   58450   59641    1    525871     1   11911

19801   1   72673   74014    1    537782     1   13411

19901   3   57786   58990    1    551193     1   12041

20001   1   72810   74165    1    563234     1   13551

20101   1   71464   72790    1    576785     1   13261

20201   3   71588   72709    1    590046     1   11211

20301   3   63014   64235    1    601257     1   12211

20401   1   72637   73883    1    613468     1   12461

20501   1   72401   73679    1    625929     1   12781

20601   1   68737   70032    1    638710     1   12951

20702   1   59347   60283    1    651661     1    9361

20802   3   60465   61289    1    661022     1    8241

20902   1   61483   62401    1    669263     1    9181

21002   3   62706   63521    1    678444     1    8151

21102   1   63709   64590    1    686595     1    8811

21202   3   64741   65541    1    695406     1    8001

21302   1   65726   66602    1    703407     1    8761

21402   3   66868   67633    1    712168     1    7651

21502   1   67800   68634    1    719819     1    8341

21602   3   68855   69609    1    728160     1    7541

21702   1   64867   65837    1    735701     1    9701

21802   3   66112   66819    1    745402     1    7071

21901   1   67035   67947    1    752473     1    9121

22001   3   68098   68788    1    761594     1    6901

22101   1   59957   60785    1    768495     1    8281

22201   3   61284   61971    1    776776     1    6871

22301   1   62142   62900    1    783647     1    7581

22401   3   63070   63729    1    791228     1    6591

22501   1   63931   64736    1    797819     1    8051

22601   3   64902   65557    1    805870     1    6551

22701   1   65756   66504    1    812421     1    7481

22801   3   66724   67361    1    819902     1    6371

22901   1   67584   68305    1    826273     1    7211

23001   3   68466   69090    1    833484     1    6241

23101   1   69328   70002    1    839725     1    6741

23201   3   70176   70800    1    846466     1    6241

23301   1   70959   71600    1    852707     1    6411

23401   3   71799   72373    1    859118     1    5741

23501   1   59500   59991    1    864859     1    4911

23502   1   64816   64975    1    869770     1    1591

23601   3   60184   60739    1    871361     1    5551

23701   1   60894   61494    1    876912     1    6001

23801   3   61736   62291    1    882913     1    5551

23901   1   62467   63049    1    888464     1    5821

24001   3   63199   63737    1    894285     1    5381

24101   1   63900   64454    1    899666     1    5541

24201   3   64652   65177    1    905207     1    5251

24301   1   65350   65885    1    910458     1    5351

24401   3   66125   66625    1    915809     1    5001

24501   1   67102   67626    1    920810     1    5241

24601   3   67804   68297    1    926051     1    4931

24701   1   68481   68985    1    930982     1    5041

24801   3   69168   69653    1    936023     1    4851

24901   1   69811   70304    1    940874     1    4931

25001   3   70595   71066    1    945805     1    4711

25101   1   71288   71769    1    950516     1    4811

25201   3   71928   72392    1    955327     1    4641

25301   1   70020   70469    1    959968     1    4491

25401   3   70640   71087    1    964459     1    4471

25501   1   59595   60040    1    968930     1    4451

25601   3   60220   60650    1    973381     1    4301

25701   1   60824   61247    1    977682     1    4231

25801   3   61770   62192    1    981913     1    4221

25901   1   62369   62795    1    986134     1    4261

26001   3   62988   63392    1    990395     1    4041

26101   1   63595   63989    1    994436     1    3941

26201   3   64183   64558    1    998377     1    3751

26301   1   64733   65098    1   1002128     1    3651

26401   3   65258   65615    1   1005779     1    3571

26501   1   65790   66143    1   1009350     1    3531

26601   3   66666   67019    1   1012881     1    3531

26701   1   67204   67549    1   1016412     1    3451

26801   3   67737   68070    1   1019863     1    3331

26901   3   68376   68711    1   1023194     1    3351

27001   1   68865   69178    1   1026545     1    3131

27101   3   69315   69634    1   1029676     1    3191

27201   1   69786   70086    1   1032867     1    3001

27301   3   70227   70524    1   1035868     1    2971

27401   1   70669   70961    1   1038839     1    2921

27501   3   71098   71380    1   1041760     1    2821

27601   1   71524   71795    1   1044581     1    2711

27701   3   71939   72193    1   1047292     1    2541

27801   3   65320   65554    1   1049833     1    2341

27901   1   65694   65945    1   1052174     1    2511

28001   3   66094   66302    1   1054685     1    2081

28101   1   66456   66683    1   1056766     1    2271

28201   3   66822   67024    1   1059037     1    2021

28301   1   67173   67378    1   1061058     1    2051

28401   3   67523   67710    1   1063109     1    1871

28501   1   67869   68052    1   1064980     1    1831

28601   3   68401   68573    1   1066811     1    1721

28701   1   68744   68932    1   1068532     1    1881

28801   3   69080   69242    1   1070413     1    1621

28901   1   67499   67657    1   1072034     1    1581

29001   3   67196   67341    1   1073615     1    1451

29101   1   66922   67069    1   1075066     1    1471

29201   3   66623   66757    1   1076537     1    1341

29301   1   66378   66502    1   1077878     1    1241

29401   3   66085   66198    1   1079119     1    1131

29501   1   65859   65964    1   1080250     1    1051

29601   3   65590   65688    1   1081301     1     981

29701   1   65366   65451    1   1082282     1     851

29801   3   65114   65195    1   1083133     1     811

29901   1   64875   64957    1   1083944     1     821

30001   3   64628   64714    1   1084765     1     861

30101   1   64392   64479    1   1085626     1     871

30201   3   64137   64219    1   1086497     1     821

30301   1   63912   63997    1   1087318     1     851

30401   3   63643   63726    1   1088169     1     831

30501   1   63416   63504    1   1089000     1     881

500101   2   69689   70298    1   1089881     1    6091

500201   4   70499   71137    1   1095972     1    6381

500301   2   71287   71903    1   1102353     1    6161

500401   4   72121   72720    1   1108514     1    5991

500501   2   58198   58428    1   1114505     1    2301

500601   4   58676   59021    1   1116806     1    3451

500701   2   59301   59707    1   1120257     1    4061

500801   4   59987   60479    1   1124318     1    4921

500901   2   60702   61280    1   1129239     1    5781

501001   4   61549   62211    1   1135020     1    6621

501101   2   62464   63217    1   1141641     1    7531

501201   1   70083   71005    1   1149172     1    9221

DIGITAL ARCHIVE DESCRIPTION OF GRID DATA

CLIENT                       U.S.G.S

NAME OF SURVEY               AEROMAGNETIC SURVEY of CALIFORNIA

AREA NAME                    DEATH VALLEY

CONTRACTOR                   FUGRO AIRBORNE SURVEYS

JOB CODE                     655

GRID ARCHIVE NAME            CALIF_TF.GRD

FORMAT                       GEOSOFT BINARY GRID

CONTENT                      TOTAL MAGNETIC INTENSITY

CREATION DATE                February 15, 2001

NUMBER of ROWS and COLUMNS   704 640

PIVOTAL POSITION (X,Y)       470022 3978828

CELL SIZE                    133m

UNIT                         nT

UNIT FACTOR                  0.001

MINIMUM VALUE (nT)           -540.011

MAXIMUM VALUE (nT)            394.056

MEAN VALUE (nT)              -101.347

GRID ARCHIVE NAME            CALIF_RADAR.GRD

FORMAT                       GEOSOFT BINARY GRID

CONTENT                      RADAR

CREATION DATE                March 7, 2001

NUMBER of ROWS and COLUMNS   704 640

PIVOTAL POSITION (X,Y)       470022 3978828

CELL SIZE                    133m

UNIT                         m

UNIT FACTOR                  0.01

MINIMUM VALUE (m)            168

MAXIMUM VALUE (m)            1217 (instrument maximum)

MEAN VALUE (m)               869

PROJECTION INFORMATION :

DATUM                                 NAD83

SHEROID                               WGS84

PROJECTION                            UTM

CENTRAL MERIDIEN                      117 West

FALSE EASTING                         500000 m

FALSE NORTHING                        0 m

SCALE FACTOR                          0.9996

# Footnotes

Pilkington, M., and Thurston, J. B., 2001.  Draping corrections for aeromagnetic data: line versus grid based approaches; Exploration Geophysics, in press.

Minty, B.R.S., 1991: Simple micro-levelling for aeromagnetic data; Exploration Geophysics, v.22, p. 591-592.