I. CONTENTS

SUBFOLDERS: GRID_GRD, GRID_TIFF

FILES IN SUBFOLDERS:

| FILE NAME | UNITS | DESCRIPTION |
| --- | --- | --- |
| FtIrwinAEM_RhoDOI_4m | ohm-m | Inverted resistivity from model layer 1, center depth = 4 m |
| FtIrwinAEM_RhoDOI_13m | ohm-m | Inverted resistivity from model layer 2, center depth = 13 m |
| FtIrwinAEM_RhoDOI_23m | ohm-m | Inverted resistivity from model layer 3, center depth = 23 m |
| FtIrwinAEM_RhoDOI_33m | ohm-m | Inverted resistivity from model layer 4, center depth = 33 m |
| FtIrwinAEM_RhoDOI_45m | ohm-m | Inverted resistivity from model layer 5, center depth = 45 m |
| FtIrwinAEM_RhoDOI_58m | ohm-m | Inverted resistivity from model layer 6, center depth = 58 m |
| FtIrwinAEM_RhoDOI_72m | ohm-m | Inverted resistivity from model layer 7, center depth = 72 m |
| FtIrwinAEM_RhoDOI_88m | ohm-m | Inverted resistivity from model layer 8, center depth = 88 m |
| FtIrwinAEM_RhoDOI_105m | ohm-m | Inverted resistivity from model layer 9, center depth = 105 m |
| FtIrwinAEM_RhoDOI_123m | ohm-m | Inverted resistivity from model layer 10, center depth = 123 m |
| FtIrwinAEM_RhoDOI_144m | ohm-m | Inverted resistivity from model layer 11, center depth = 144 m |
| FtIrwinAEM_RhoDOI_167m | ohm-m | Inverted resistivity from model layer 12, center depth = 167 m |
| FtIrwinAEM_RhoDOI_192m | ohm-m | Inverted resistivity from model layer 13, center depth = 192 m |
| FtIrwinAEM_RhoDOI_219m | ohm-m | Inverted resistivity from model layer 14, center depth = 219 m |
| FtIrwinAEM_RhoDOI_249m | ohm-m | Inverted resistivity from model layer 15, center depth = 249 m |
| FtIrwinAEM_RhoDOI_282m | ohm-m | Inverted resistivity from model layer 16, center depth = 282 m |
| FtIrwinAEM_RhoDOI_318m | ohm-m | Inverted resistivity from model layer 17, center depth = 318 m |
| FtIrwinAEM_RhoDOI_358m | ohm-m | Inverted resistivity from model layer 18, center depth = 358 m |
| FtIrwinAEM_RhoDOI_379m | ohm-m | Inverted resistivity from model layer 19, center depth = 379 m |
| FtIrwinAEM_RhoDOI_Color5to500log.zon |  | Geosoft color zone file, scale = 25 to 5000 logarithmically increasing (GRID_GRD folder only) |

COORDINATE SYSTEM:

HORIZONTAL:

Universal Transverse Mercator projection

Zone 11 North

North American Datum of 1983 (NAD83)

II. EXPLANATION

III. DISCLAIMERS

Although these data have been subjected to rigorous review and are substantially complete, the USGS reserves the right to revise the data pursuant to further analysis and review.  Furthermore, the data are released on condition that neither the USGS nor the United States Government may be held liable for any damages resulting from its authorized or unauthorized use.

Although these data have been processed successfully on a computer system at the U.S. Geological Survey, no warranty, expressed or implied, is made regarding the display or utility of the data on any other system or for general or scientific purposes, nor shall the act of distribution constitute such warranty.  The U.S. Geological Survey shall not be held liable for improper or incorrect use of the data described and/or contained herein.

Although this information product, for the most part, is in the public domain, it also contains copyrighted materials as noted in the text. Permission to reproduce copyrighted items for other than personal use must be secured from the copyright owner.

Any use of trade, product, or firm names is for descriptive purposes only and does not imply endorsement by the U.S. Government.