I. CONTENTS

FILES IN DIRECTORY:

AIRBORNE ELECTROMAGNETIC AND MAGNETIC DATA:

FtIrwinAEM_DATA.XYZ

FtIrwinAEM_DATA.gdb

COORDINATE SYSTEM:

HORIZONTAL:

Universal Transverse Mercator projection

Zone 11 North

North American Datum of 1983 (NAD83)

VERTICAL:

North American Vertical Datum of 1988 (NAVD88)

NAVD88 elevations are derived from the USGS National Elevation Dataset (NED), 30-m resolution

II. DATABASE FORMAT

| CHANNEL | UNITS | DESCRIPTION |
| --- | --- | --- |
| line | - | Line number |
| flight | - | Flight number |
| emfid | - | fiducial |
| utctime | hh:mm:ss.s | UTC time |
| X_mag | m | Easting position of magnetic sensor (NAD83), UTM Zone 11 North |
| Y_mag | m | Northing position of magnetic sensor (NAD83), UTM Zone 11 North |
| X_EM | m | Easting position of EM sensor (NAD83), UTM Zone 11 North |
| Y_EM | m | Northing position of EM sensor (NAD83), UTM Zone 11 North |
| NED30_mag | m | Land-surface elevation at magnetometer position referenced from the NED |
| NED30_bird | m | Land-surface elevation at EM sensor position referenced from the NED |
| galt_mag | m | GPS-derived elevation of magnetic sensor |
| galt_EM | m | GPS-derived elevation of EM sensor |
| lalt | m | Laser altimeter, terrain clearance of the EM sensor |
| ralt_lag | m | Radar altimeter, lag corrected, terrain clearance of the helicopter |
| Ralt_GPS_Separation | m | Geometric separation from radar altimeter to GPS on magnetometer |
| Tow_cable_length | m | Length of cable between helicopter and EM sensor |
| baro | mbar | Barometric pressure |
| balt | m | Barometric altitude of the EM sensor |
| bheight | m | Terrain clearance of the EM sensor calculated from ralt and galt_mag |
| pitch | degree | Pitch of the EM sensor |
| roll | degree | Roll of the EM sensor |
| yaw | degree | Yaw of the EM sensor |
| basemag | nT | Base station total magnetic intensity |
| magU_raw | nT | Raw magnetic intensity |
| magU_filt | nT | Filtered magnetic intensity |
| magU | nT | Diurnally corrected magnetic intensity |
| magUf | nT | Final leveled total magnetic intensity |
| IGRF | nT | International Geomagnetic Reference Field (IGRF) |
| magUf_igrf | nT | Final leveled total magnetic intensity, IGRF removed |
| Inclination | degree | Magnetic inclination |
| Declination | degree | Magnetic declination |
| pwrline | - | Power line monitor |
| Zon_client | nT/s | Raw streaming on-time Z component, [i] = array index |
| Zoff_client | nT/s | Raw streaming off-time Z component, [i] = array index |
| Zon_lag | nT/s | Lagged streaming on-time Z component, [i] = array index |
| Zoff_lag | nT/s | Lagged streaming off-time Z component, [i] = array index |
| lZon | nT/s | Leveled, lagged streaming on-time Z component, [i] = array index |
| lZoff | nT/s | Leveled, lagged streaming off-time Z component, [i] = array index |
| Zon_miclev | nT/s | Microleveled, lagged streaming on-time Z component, [i] = array index |
| Zoff_miclev | nT/s | Microleveled, lagged streaming off-time Z component, [i] = array index |
| Xoff | nT/s | Raw streaming off-time X component, [i] = array index |
| lxoff | nT/s | Leveled, lagged streaming off-time X component, [i] = array index |
| TranOn | ms | Transmitter turn-on time, relative to reference time zero |
| TranOff | Ms | Transmitter turn-off time, relative to reference time zero |
| TranPeak | Amp | Transmitter peak current |
| TranSwitch | ms | Transmitter peak current time, relative to reference time zero |

III. DISCLAIMERS

Although these data have been subjected to rigorous review and are substantially complete, the USGS reserves the right to revise the data pursuant to further analysis and review.  Furthermore, the data are released on condition that neither the USGS nor the United States Government may be held liable for any damages resulting from its authorized or unauthorized use.

Although these data have been processed successfully on a computer system at the U.S. Geological Survey, no warranty, expressed or implied, is made regarding the display or utility of the data on any other system or for general or scientific purposes, nor shall the act of distribution constitute such warranty.  The U.S. Geological Survey shall not be held liable for improper or incorrect use of the data described and/or contained herein.

Although this information product, for the most part, is in the public domain, it also contains copyrighted materials as noted in the text. Permission to reproduce copyrighted items for other than personal use must be secured from the copyright owner.

Any use of trade, product, or firm names is for descriptive purposes only and does not imply endorsement by the U.S. Government.